Purpose:
This test simulates the real traffic of the WR network, in order to measure the delay of the telegrams in each VLAN.
Explanation:
The WR network contains the following traffic:
(1) DM VLAN broadcast 100Mbps 11 packets/100us (3-5 normal)
(2) DM VLAN unicast 10Mbps 3 packets/300us + 2 B2B packets/10ms
(3) B2B VLAN 10 packets/10ms totally 28 packets/s
(4) Low priority noise broadcast random 10Mbps
Table 1. The list of the traffic for all VLANs
VLAN name	Type	Payload length	VLAN ID	Priority	Traffic
DM VLAN	broadcast	110 bytes	7	7	100Mbps 11 packets/100us
DM VLAN	unicast	110 bytes	7	7	10Mbps 3 packets/300us / 4packets/s 2 B2B packets/10ms
B2B VLAN	broadcast	110 bytes	6	6	28 packets/s 10 packets/10ms
Other VLAN	broadcast	Random	5	5	Random 10Mbps

Test configuration:
Port 1: Input DM traffic
Port 2: Input B2B traffic
Port 4: Input Low priority traffic
Configuration of the VLAN
1.Use PUTTY to login to the timing server timing@tsl006.acc.gsi.de
2.Login the wr switch root@wrip
3.Copy the VLAN_config.sh to the WR switch
4.Run ./VLAN_config.sh
Configuration of Xena 2G
1. Open Xena2M
2. Load configuration file /Network_simulation/WRnetwork_simulation_Xena_configuration/Xena2M_config.xmcfg