Xena_switch connection:
4 switches
1st switch connects 6 xena ports: 0-0-0 to 0-0-5
2nd switch connects 4 xena ports: 0-2-0 to 0-2-3
3rd switch connects 4 xena ports: 0-2-4 to 0-2-5, 0-4-1 to 0-4-1
4th switch connects 4 xena ports: 0-4-2 to 0-4-5

Xena port 0-0-0 produces DM VLAN packets. Broadcast: stream 0/0 Unicast: stream 0/1
Xena port 0-4-4 produces low priority traffic. stream 0/4
Xena port 0-4-5 produces B2B VLAN. Broadcast: stream 0/3 Unicast:stream 1/5

The test was running for 14.5 hours. No packet loss.
WR / switch	DM VLAN Broadcast	DM VLAN Unicast	B2B VLAN	Low priority VLAN
1 switch	16.270us ± 13.590us	16.126us ± 13.398us	30.005us ± 27.325us	33.838us±31.086us
2 switches	17.825us ± 13.807us	17.825us ± 13.590us	31.654us ±27.662us	35.345us±30.917us
3 switches	20.688us ± 13.951us	20.616us ± 13.783us	34.495us ± 27.734us	38.280us ± 31.382us
4 switches	23.502us ± 14.192us	23.358us ± 13.879us	37.261us ± 27.854us	41.046us ± 31.158us