Test explanation:

Working principle of Xena:
===================================================================================
Rate Test:
Full Mesh (18 ports are used)
Each Xena port generates 17 streams, each of them is with 500Mbps/17 =29.4Mbps and unicast. So each WR switch port transfers 500Mbps unicast traffic and receives 29.4Mbps*17=500Mbps traffic.

Part Mesh 1:N (e.g. N=17)
Xena port 1 generates 17 streams, each of them is with 500Mbps/17 =29.4Mbps and unicast.
Part Mesh N->N (e.g. N=9)
Each port in West generates 9 streams, each of them is with 500Mbps/9 Mbps and unicast.
===================================================================================
Congestion Control:
Test principle:
Two source ports: port 0 and 1. Two destination ports: port 2 (uncongesgted) and 3 (congested).
Port 0 produces 2 streams, the 1st is with half bandwidth (500Mbps) and to destination port 2, the 2nd is with half bandwidth (500Mbps) and to destination port 3. Port 1 produces one stream with full bandwidth (1Gbps) and to destination port 3.
If the uncongested port 2 dose not loss packets, the switch has the congestion control.
===================================================================================
Forward Pressure:
Test principle:
Port 1 produces packets with the Inter-Frame Gap (IFG) less than 20 Bytes to the destination port 2.
Xena uses the different definition of the Inter-Frame Gap (IFG). The IFG denotes all the space between two packets, including the seven-byte preamble, the one-byte Start Frame Delimiter and the (minimum) 12 byte Inter-Packet Gap. This gives the 20 byte used by the Xena testers.
For the Forward pressure test, the standard does not specify to use a minimum IPG of 96 bits. Test frames should be transmitted to the port of the DUT with an IFG 19 bytes, which is configured by the Interframe Gap Delta. The default IFG Delta is 1 byte, which gives the 19 bytes IFG.
With the IFG 20 bytes, the bit rate for frame (bit rate L1) is 761Mbps, the bit rate for frame+IFG (bir rate L2) is 985Mbps.
With the IFG 19 bytes, the bit rate L1 is 770Mbps, the bit rate L2 is 998Mbps.
Tx Max Util = Tx bit rate L2 for IFG 19 Bytes/Bit rate L2 for IFG 20 Bytes
Rx Max Util = Rx bit rate L2 for IFG 19 Bytes/Bit rate L2 for IFG 20 Bytes
If the destination port of the switch egresses packets with IFG bigger than 20 bytes, there is no forward pressure for the switch and it is allowed for the packet loss. Good switch should be detected no forward pressure.
===================================================================================
Max Forward Rate:
Port 1 produces one stream with sweep bandwidth to the destination port to find the maximum forward rate (frames per second). Rx Rate (L1) (Bit/s) tells the Max forward rate.
===================================================================================
Addresses Caching Capacity:
Test port sends one telegram to the Listening port and listening port send the listening frame to the test port, now the Route table has two items, test port MAC and port No, listening port MAC and port No. Than the test port sends packets with different Src Mac (Mac1) and listening port Des Mac. And the listening port sends the listening frame with Des Mac (Mac1). When the addresses cache is full, the listening frame will be broadcasted to the monitor port.
For 2 layer switch, the cache size is 20K.
===================================================================================